## Slide 1: Lecture 3: Multiphase
EAS 7970: Multiphase Subsurface Fluid Flow
L. M. Cathles
Tammo Steenhuis
Larry Brown
Spring 2017
3160 Snee Hall

## Slide 2: Generalize to non-aqueous
Momentum Equation
Continuity Equation
Constitutive Relations
Diffusion Equation
Hydrology/water
Fluid phase a

## Slide 3: Relationship to Darcy’s Law
K’[m2] = K[m s-1] / 107
Note: Hydrologists specialize to water, planet earth and 20°C.
mw(0°C)=1.78x10-3 Pa s

## Slide 4: Horner plot analysis
From lecture 2 slide 11
Oil patch
Packed off interval
Measure pressure
Slope gives transmissivity
Famous well analysis texts

## Slide 5: Multiphase- capillary pressure (the simple view)
oil
water
Oil likes oil more than water
Interface behaves like a stretched rubber sheet
oil-water surface* tension, g , molds oil into sphere like a balloon
Pressure inside oil is greater than in water by capillary pressure, pc
Force balance gives the pressure
Oil must be pushed into a finer strata
Water gets “sucked in” or imbibed
pc greater for smaller oil bubbles
bubble size determined by pore size
entry pressure
* or interfacial tension
Note: water is assumed to “wet” the solid surface

## Slide 6: Multiphase
Force driving petroleum same as that driving water
  + buoyancy term causing lighter petroleum to rise
  + capillary term pushing petroleum out of finer pores
up positive
points down
- points up
grad 1/r increases into pore
- grad 1/r pushes oil out
Oil is buoyant
pc pushes oil out of fine pores

## Slide 7: But water is also sucked into fine pores if surface is hydrophilic (water wet)
Capillary tube illustration
Tree rootlets do the (can “suck” at -40 bars)
Note: cos ϴ is wetting angle
Often assumed: cos ϴ ~ 1

## Slide 8: Contact angle indicates surface preference
Contact angle between liquid drop and surface (measured from the liquid-solid surface)
Hydrophilic or water wet
water
hydrophobic
Material can be both oil and water wet
*
* The force balance argument is tricky and probably requires a thermodynamic perspective which we will sidestep here

## Slide 9: Liquid oil and water on Haynesville gas shale
Engelder et al.(2014)

## Slide 10: Imbibition of water into Marcellus Shale
Engelder et al.(2014)
Notice gas is expelled as water is imbibed
How can a sediment be both water and oil wet?

## Slide 11: Imbibition and drainage (always relative to water)
Drainage (of water) , e.g. inject gas
Entry pressure of gas, pc=pg-pw,
pw=0 at entry surface
When imbibe water, not all gas can exit
…end effect in column tests
Cannot push gas into 100% of pores
Imbibition not same as drainage curves
(because gas left behind)
vacuum
Packed
column
porous plate
pc=pnw-pw
Siw
Sinw

## Slide 12: Example:
Steel plug L meters long with three holes

## Slide 13
Thus, as we force oil into the steel plug by increasing po, we obtain a crude drainage curve
If we then lower the pressure on the oil the water will imbibe first in the small pore, then in the middle, and then in the large, producing an identical imbibition curve

## Slide 14
If the oil introduced into the large pore causes it to become fully oil wet (e.g., ϴ=180°), po must be negative to pull the oil out of this last pore.
Sometimes introducing oil will cause part of a core to become oil wet.

## Slide 15
Hysteresis can occur even in one pore model.
When pressure is sufficient for oil to enter the narrow pore, oil will also fill all the wider parts of that pore.
But when po is reduced, water will not imbibe into wider parts until oil pressure is reduced below the oil entry pressure there.

## Slide 16: Relative permeability
Unconsolidated
sand
Consolidated
sand
Siw
Sinw
Why fall steeply?
Why not fall steeply?
For permeability of A, turn other phase into rock

## Slide 17: Fluid Properties
To calculate, we need fluid properties

## Slide 18: Viscosity of water
At 20°C the dynamic viscosity is 1.0x10-3 Pa s. At 100°C it is 0.28x10-3 Pa s, less than 1/3rd the 20°C viscosity. To good approximation between 0 and 150°C:

## Slide 19: Viscosity of oil = f(T,GOR,API)
Empirical relationships have been discovered that describe oil viscosity. For example, Beggs and Robinson (1974) showed that dead (mdo) and live (mo) viscosity in centipoise (1 cp=10-3 Pa s) can be described as a function of temperature (TF[°F]), GOR (gas oil ratio in scf /bbl ), and oil density in API:
API gravity (oil density) is a function of oil maturity (how thoroughly the oil has been cooked). Ultimately oil cooks to methane plus a residual, but on the way the oil progresses from heavy (e.g., high density) viscous oil, to light oil. API gravity was an early way to conveniently compare the density of oil and water.

## Slide 20: GOR of Oil
Typically oil contains sufficient gas that as it migrates upward (it is less dense than water) it expels gas. When it reaches a reservoir it is therefore commonly gas saturated. The oil contains just the amount of gas such that it is at its bubble point—gas is just on the verge of “bubbling” out of the oil. In other words the reservoir pressure equal the bubble point of the oil. The bubble point of oil depends on TF, GOR, and API:
Glasø(1980)
For pb=preservoir, we can invert to obtain GOR

## Slide 21: Phase Diagrams
On Blackboard to read

## Slide 23: A calculator is on eas-cathles
Oil is at 2 km depth
Pressure is hydrostatic
T=60C, p=200 bars
Bubble point is 200 bars
GOR=766 scf/bbl
Live viscosity = 0.00042 Pa s
Note: some of these are for startup initial values. Numbers are slightly different when spin. For example after spin up and back, GOR=856.7 but live viscosity is still 4.2=10-4 Pa s.
Now let’s see how a carrier bed might operate for a reasonable oil generation rate.

## Slide 24: Carrier bed calculation
Darcy sand, k’= 10-12 m2
m=4.2x10-4 Pa s
2°
Source rock of thickness h
h
GK=0.02 maturable pet/kg sed
h=100 m source thickness
1500 m maturation interval
fo 0.55
fs 0.1
rsed 2400 kg m-3
rpet 800 kg m-3
Need:
Very thin layer of oil migrates along top of carrier sand!

## Slide 25: In 1987 Dave Powley of Amoco raised issue of pressure compartmentation with GRI
Powley 1987 presentation to Gri

## Slide 26: TOOP in GoM
Powley 1987 presentation to Gri
Powley’s Buried
Beer Bottle
Model
Al Saieb, Anadarko Basin

## Slide 27
Bradley and Powley (1990)
Powley (1990)
10 years of evidence

## Slide 28
Bradley and Powley (1990)

## Slide 29
Sacramento Valley, Ca
Hunt (1990)
North Sea
GRI Verification

## Slide 30: Pockmarks and seepages
Pockmarks produced by gas-driven water venting

## Slide 31: Echo Sounder Records of Gas Plumes in the Water Column of the Hydrate Ridge Region
Trehu A M et al ,2003
Gas plumes are fairly common

## Slide 32
http://oceanlink.island.net/ONews/ONews7/images/mud%20vol%20-%20FBGNMS.jpg
Mud Volcano
gas
Salt dome
Brine pool
Methanotrophic mussels
Ian MacDonald (TAMU)
Worms grazing on bacteria
growing on surface of methane ice
Ian MacDonald (TAMU)
Ian MacDonald (TAMU)

## Slide 33
Callogoria coral; cup coral
Small oil droplets
adhering to hydrate
Ian MacDonald (TAMU)
Ian MacDonald (TAMU)
http://i.livescience.com/images/090407-deep-vent-02.jpg
Mineral chimney and microbe mats
Madrepora coral
Mississippi Canyon
Oceanexplorer.noaa.gov

## Slide 34: Reservoir (capillary) seals
How would they work?

## Slide 35: Assignment
Read p 14-20 of Cathles and Adams (2005) on blackboard
Experiment with calculator
Seek to understand how Petrel handles fluid and material properties