## Slide 1: Tracers- documentation of flow through rocks
Lecture 20
EAS/ChemE 6669 Earth Energy Science and Engineering
by
L. M. Cathles
November 20, 2015
2146 Snee Hall
Notes: 1

## Slide 2: Outline
Subsurface flow is complicated
Why tracers

## Slide 3: Permeability is just the start
Dh
L
A. Permeability
B. Geometry
C. Geology
Toth (1962)
Freeze and Witherspoon (1967)
equipotentials
Flow lines
Darcy (1856)

## Slide 4: Veins are fractures cemented by fluid flow and mineral precipitation
A
B

## Slide 5: Spectacular examples of joint can be seen in our Ithaca gorges.

## Slide 6: Gold
El Indeo
Few things motivate like Au
Gold has very low solubility and spectacular deposition such as shown requires very high volumes of fluid flow

## Slide 7: The Mother Lode, Ca
m wide vein strikes across countryside formed by a different mechanism
Gold rush
1848-1855
Regional fluid escape formed Mother Lode

## Slide 8: Why Tracers?
Connectivity
Flow porosity
Diffusional accessibility

## Slide 9
seeps
Horizontal crack at 8 m depth
7 m
204
104
304
404
Cambrian sandstone
1% porosity
Chasm Lake
Chasm Lake
Altona, NY: connectivity in a single crack
Crack(s)
1.9 mm

## Slide 10
#2
7 m
204
104
304
404
6
504
204 404 304
104
#2
#3
#5
#6
C-dots
I
5
7
3
Calibration
pair
2
#7
(77%)
(75%)
(60%)
(63%)
(60%)
(58%)
(1%)
(4%)
(51%)
(59%)
(51%)
(62%)
(16%)
(18%)
(60%)
low
hi
barrier
barrier
barrier
barrier
Single crack flow is complicated!

## Slide 11: Palinpinon Geothermal Field, Philippines
Main production interval
Injection wells
Production Wells

## Slide 14
Only P5R (Black) arrives

## Slide 15: Model
Conclusions
Flow porosity ~0.01%
Flow remarkably homogeneous
  (complications- recirculation of tracer)

## Slide 16: Interpretation reasonable
Darcy’s Law
Intrinsic permeability
Fracture Porosity
D =0.1 m
d[mm] | k’[m2] | k’[md] | ff[%]
1 | 3.33x10-18 | 3.33x10-3 | 0.002
10 | 3.33x10-15 | 3.33 | 0.02
100 | 3.33x10-12 | 3330 | 0.2
How could one test it?

## Slide 17: Dual Tracer Concept
Chemical Tracer
Injection

## Slide 18: Inert nanoparticle synthesis
C-dot nanoparticles
Citric Acid
Ethanolamine
mix at room temperature
OH
OH
HO
Dry
Pyrolyze at 200°C for 8 hrs
Dialyze to remove ~3 nm particles
Detect by fluorescence to ~10 ppb
DC-dot=1.2x10-6 cm2 s-1 = 0.1 cm2 d-1 = 0.01 cm2 d-1
DKBr =2x10-5 cm2 s-1 = 1.7 cm2 d-1 = 0.17 cm2 d-1
TEM
@20°C
@130°C
diffuse 17 times more slowly

## Slide 19: Methods tested in column experiments
Hele-Shaw Cell
And sand cells and columns
Ceffluent(t)/Co
Model Analysis
∩
∩
Subramanian et al (2013)
L
l
l
L
t
l
Design rule:
=
O.17 core PV/d
497 core PV/d

## Slide 20: Successful test in Ghawar Reservoir
Field test 86% recovery
water 5 kg mix 130 ppm
255 bbl with 130 ppm C-Dot
injected at 7090 ft into 50 ft interval of
20% porosity carbonate reservoir at
~100°C and 120,000 TDS pore fluids.
Shut in 2 days.
Produced ~6000 bbl.
86% recovery.
Kanj, Rashid and Gianelis, 2011, SPE 142592-PP

## Slide 21: Successful test in quartzite, Altona NY
Yushi Zhou, 2014 Cornell Ph.D Thesis
Horizontal crack at 8 m depth
7 m
Iodide =
C-Dot
…C-dots behaved like Iodine
EPA and DEC permissions obtained
Photo bleaching corrected
Laplace methods used in interpretation

## Slide 22: The Ely Witch Experiment
…testing the diffusional access of copper to in situ leaching
Cathles et al. (1974)

## Slide 23: The Idea
Tracer arrives when it displaces the pore volume it interacts with once
Cathles et al. (1974)

## Slide 24: The site: Pit bench at Ray Mine, Ely Nevada
Injection well
other wells
bailed
B’
B
3400 gal injected
Rate 182 gal/d
Over 50’ interval
41,000 ppm NaCl
0.5mm SiO2 dust
50 ft
26 d
Cathles et al. (1974)

## Slide 25: Predictions
Injection rate | 182 gal d-1
Volume injected | 3400 gal
Fracture volume | 1057 gal (31%)
Halo volume | 105,760 gal (3100%)
D1/2 | 0.15 m
d1/2 | 75mm
D’NaCl | 2x10-9 m2 s-1
D’particles | 10-12 m2 s-1
tD-NaCl=tD1/22/D’NaCl | 651 d
tD-particles=tD1/22/D’particles | 1.3x106 d
tH= vol. halo/inj. rate | 581 d
tf = vol fx/inj. rate | 5.8 d
t | 30 d
R=30 ft
Cathles et al. (1974)

## Slide 26
Chart: Predictions
| 1.0000000000000007E-2 | 2.0000000000000014E-2 | 3.0000000000000016E-2 | 4.0000000000000029E-2 | 5.0000000000000031E-2 | 7.0000000000000034E-2 | 8.5000000000000048E-2 | 0.1 | 0.15000000000000024 | 0.25 | 0.5 | 0.75000000000000122 | 1 | 1.25 | 1.5
value | 0 | 0 | 4.47e-05 | 0.0004206 | 0.00161 | 0.00754 | 0.0153 | 0.0257 | 0.0685 | 0.157 | 0.318 | 0.414 | 0.48 | 0.527 | 0.564
Equation (5b)
valid to t~tD
5x10-5
NaCl tracer
tortuosity
effective diffusion constant = Dofm/t
half fracture spacing
matrix porosity
fracture transit time
Cathles et al. (1974)

## Slide 27
SiO2 particles arrived
3400 gallons injected
over 30 days
Gallons at particle arrival
arrival K277
later
analyzed
Cathles et al. (1974)

## Slide 28: Salt never arrived
NaCl never arrived
injected 41,000 ppm NaCl
Cathles et al. (1974)

## Slide 29: Example: Ekofisk Chalk
Ekofisk (N Sea chalk) permeability
  Matrix 0.5-10 md
  Effective up to 100 md
  Fx spacing (5)-15-100 cm
  intense in faults
  conjugate, healed
  induced
Anderson (1995, esp. Table 3.1)

## Slide 30: Diffusion in rock
Stokes-Einstein Equation
Boltzmann
constant
Dynamic (shear)
viscosity of water
Particle
diameter
F/m2
F-m
Pau et al. (J. Phys. Chem., 1990,94, 2671)
 | dslip[nm] | D[cm2 d-1]20C | D[cm2 d-1]20C measured | x[cm]=2(D20Ct)0.5 | 
 |  |  |  | t=1d | t=10d
He |  |  |  |  | 
Cl- | 0.181 | 2.04 | 1.53 | 2.9 | 9
Na+ | 0.276 | 1.34 | 1.00 | 2.3 | 7.3
np | 3 | 0.12 |  | 0.7 | 2.2
np | 30 | 0.012 |  | 0.2 | 0.7

## Slide 31: Transit time between wells
2xo | T[d]
10 | 3
50 | 80
100 | 322

## Slide 32: Diffusion fill time
 | 20C | 50C | 130C
D[cm/d] | 2 | 4.2 | 13.4
d | 20C | 50C | 130C
5 | 2.3 days | 1.1 | 0.35
10 | 9.3 | 4.5 | 1.4
50 | 234 | 111 | 35
100 | 937 | 446 | 140
Diffusional matrix fill time (t=3)
Diffusional diffusion constant

## Slide 33: Design Criterion for Ekofisk
20°C
50°C
130°C
Cl-
3 nm nanoparticle
20°C
50°C
130°C
3 80 322d
3 80 322d
Range Ekofisk fracture spacing
Range Ekofisk fracture spacing
Lines show combination of well and fracture spacing that meet the design criterion . The criterion applies to the most rapidly diffusing of the pair of tracers. In the left diagram this is Cl-; in the right diagram is a 3 nm diameter C-dot nanoparticle. For example, the optimum well separation for detecting fractures with 15 cm separation with Cl- in a 50°C environment is ~18 m. For 3 nm nanoparticles the well separation would be ~100 m.
Design criterion
Calculations in “Optimized tracer test conditions.xls”